## Slide 1: OBRA Training Series http://www.obraobx.com
Repeaters

## Slide 2: REPEATERS
A hand held VHF/UHF radio has a range of about 5 miles.
Obstacles such as buildings and high terrane can decrease this range.
Radio repeaters can greatly increase this range

## Slide 3: Radio Range Problem
A & B can talk, but A & B can’t talk to C.
C can’t talk to A or B.
A
B
C
Distance or Obstacles
Prevents Communications

## Slide 4: Greatly Increase Radio Range
Adding a repeater solves the problem and greatly improves the available range.
A
B
C
Repeater
- High elevation provides line of sight
for clearance above obstacles.
- Antenna is larger for better reception.
- Higher transmit power for greater range.

## Slide 5: Repeater Details
Repeaters needs to use frequency offsets.
A
B
C
A transmits on
144.550 MHz
Repeater receives on 144.550 MHz
and retransmits on 145.150 MHz
(offset of -600KHZ)
B receives on
145.150 MHz
C receives on
145.150 MHz
Repeater can’t transmit and receive on the same
frequency since the transmit signal would block
the receive signal.

## Slide 6: Repeater Details (cont.)
Repeaters Also Need a PL Tone.
A
B
C
A transmits on
144.550 MHz
PL Tone Activates Repeater.
Repeater receives on 144.550 MHz
and retransmits on 145.150 MHz
(offset of -600KHZ)
B receives on
145.150 MHz
C receives on
145.150 MHz
The PL tone is needed to access the repeater. This prevents spurious signals from activating the repeater.
Frequency assignments and tones are managed by a volunteer frequency coordinator selected by local operators.
(PL 131.8 Hz)
(PL 131.8 Hz)
(PL 131.8 Hz)

## Slide 7: Linking Repeaters Increase Range Even More
A
C
B
Repeater 1
D
E
F
Repeater 2
Repeater 1 receives from radio A and transmits to B and C but
also transmits to repeater 2 on its receive frequency allowing
Radios D,E and F to receive radio A’s transmission.
Repeater 2 does the same thing when it receives a signal from D, E or F. The result is that all radios can communicate over a greater distance. Multiple links can be used to increase range even further.

## Slide 8: OBRA Linked Repeaters These OBRA analog repeaters are always linked
Mamie TX 146.940 MHz, RC 146.340 MHz, PL 131.8 Hz
Kill Devil Hills TX 145.110 MHZ, RC 144.660 MHz, PL 131.8 Hz
Nags Head TX 145.290 MHz, RC 144.690 MHz, PL 100.0 Hz
Columbia TX 442.725 MHz, RC 447,725 MHz, PL 131.8 Hz
Buxton TX 145.150 MHz, RC 144.550 MHz, PL 131.8 Hz
Waves TX 444.325 MHz, RC 449.325 MHz, PL 131.8 Hz
Hatteras TX 442.725 MHz, RC 447.725 MHz, PL 131.8 Hz
Ocracoke TX 444.225 MHz, RC 449.225 MHz, PL 131.8 Hz
These repeaters provide communication from the Virginia border to Ocracoke